## Slide 1: Demagnetization Detection Functions
25/10/2018
Simone Ferrari (simone.ferrari@polito.it)

## Slide 2: Content
  Demagnetization functions
  Results example
  Comments

## Slide 3: Demagnetization Functions
There are 3 functions:
  demagnetizationDetectionPoint_v2
    Runs the analysis at constant temperature, for a vector of current from 0 to Imax, with ncur points
    Each point is analyzed in two rotor positions
    The critical machines are saved in the respective folder
  demagnetizationCurrentTemperature_v2
    Runs iteratively the first function on all the temperatures contained in the PMs properties
    The results from the single analysis are available, as well as a general structure
    The maximum current to keep health PMs versus the PMs temperature is computed
  plotDemagResults
    Show the portion of demagnetized PMs for a given current and temperature
  The first two functions can be runned
    Without inputs: two GUI will ask to pick the machine model and the data (maximum current, number of current point and temperature)
    With all the data in the setup structure

## Slide 4: Results example
  Result from the current-temperature analysis
  200A is the maximum current

## Slide 5: Results example
  Each folder is the result of a single temperature analysis
  DemagCurrentTemperature.mat contain all the relevant data
  Three pictures:
    Max current VS temperature
    % of demagnetized magnet against current
    % of demagnetized magnet against current and temperature (3D surface)

## Slide 6: Results example
  Critical machines contain the .fem, .ans and .png of all the critical point (at least one node below Bd)
  DemagAnalysisResult.mat contain all the relevant data
  Two pictures:
    % of demagnetized magnet against current
    Minimum PM flux density against current

## Slide 7: Comment
  Slow function:
    Extraction data from FEMM
    Current start from 0, with constant step
  Possible improvements
    Use the parallel computation on the inner cycle (current). At the moment is possible just on the outer cycle (temperature)
    Different current input. E.g. start from a certain current level and not zero
  Add function in SyR-e
    Post processing window, add one pop-up (similar to FEAfix number) with
      FEMM – single point
      FEMM – map
      Magnet – single point
      Magnet – map
      Demagnetization – single temperature
      Demagnetization – map
    The maximum current and the current steps can be easily taken from curr load and n_grid