## Slide 1: Evaluation Type
22/07/2019
Simone Ferrari (simone.ferrari@polito.it)

## Slide 2: Introduction
This document illustrates the type of FEA simulations available in post-processing window

## Slide 3: Evaluation type
The Evaluation type is set with a pop-up window in post-processing tab. The types available are:
  Single point
  Flux map
  Demagnetization Map
  Demagnetization Curve
  Characteristic current
  Flux Density Analysis
  Current Offset

## Slide 4: Single Point
This is the standard simulation. It is possible to set:
  Current amplitude
  Current angle
  PM remanence (if present)
And FEA-compute flux linkages and torque.
If vectors are used to define current, a sensitivity analysis is performed (in parallel, if pool enabled)

## Slide 5: Flux Map
It allows to perform flux maps, so flux linkages, torque and torque ripple over the dq-plane.
It always work with parallel computing, if lincenced.

## Slide 6: Demangetization Map
It perform a map in the current-temperature plane, in order to detect the critical points for the demagnetization.
The considered current vector is computed as linspace(0,Imax,Ngrid) and the temperature vector is added in temperature tab

## Slide 7: Demagnetization Curve
It evaluate the demagnetization current function of temperature. The temperature vector is defined in the proper tab, while current is iteratively computer for each temperatures

## Slide 8: Flux Density Analysis
It perform a standard simulation, with the extra information of:
  Airgap flux density along the rotor for each rotor position
  Tooth flux density, sampled along the arc that cross the middle tooth
  Stator yoke flux density, sampled in the middle of the stator yoke

## Slide 9: Current offset
It perform a standard simulation with a common mode current of 20% of the input current